## Slide 1
Computer Peripherals
CSE 315: Peripheral & Interfacing

## Slide 2: Discussion Materials:
Storage Devices
  Hard Disk Drive
  Flash Memory (PD & MC)
I/O Devices
  Displays (LCD, LED)
  Printers (DMP, IJP & LP)
  Scanners
  Pointing Devices

## Slide 3: Peripheral
Devices that are external to the main processing function of the computer
  Other than the CPU, memory, power supply
Classified as input, output, and storage
Connected via
  Ports like
    Serial, Parallel, USB etc
  Interface to systems bus like
    Small Computer System Interface (SCSI), Integrated Drive Electronics (IDE), Personal Computer Memory Card International Association (PCMCIA)

## Slide 4: SCSI (Small Computer System Interface )
Small Computer System Interface (SCSI) is a set of standards for physically connecting and transferring data between computers and peripheral devices. The SCSI standards define commands, protocols, electrical, optical and logical interfaces. SCSI is most commonly used for hard disk drives and tape drives, but it can connect a wide range of other devices, including scanners and CD drives, although not all controllers can handle all devices. The SCSI standard defines command sets for specific peripheral device types; the presence of "unknown" as one of these types means that in theory it can be used as an interface to almost any device, but the standard is highly pragmatic and addressed toward commercial requirements.

## Slide 5: SCSI (contd.)

## Slide 6: IDE (Integrated Drive Electronics)
Nominally called the IDE (Integrated Drive Electronics) bus; how ever it's more correctly known as the ATA (Advanced Technology Attachment) specification [ATA Bus]. The IDE bus is used in Personal Computers [PCs] as a hard-drive or peripheral bus to interconnect the PC mother board and a hard drive. The IDE bus is a Parallel bus. With the introduction of the Serial ATA [SATA] specification Parallel ATA [IDE] is now being called PATA.
The specification has been up-graded a number of times each building on the past specification. ATA-1 and 2 were single documents, but like SCSI, after ATA-2 the specification was divided into a number of different documents. Most maintain backward compatibility, keeping in mind the cable changed. Each new version of the standard produced an increase in bus speed. The data transfer rate is shown after each version listed below. The maximum IDE bus speed is 133MBytes/sec [133MBps].

## Slide 7: IDE (contd.)

## Slide 8: PCMCIA (Personal Computer Memory Card International Association )
In computing, PC Card is a configuration for computer parallel communication peripheral interface, designed for laptop computers. Originally introduced as PCMCIA, the PC Card standard as well as its successors like CardBus were defined and developed by the Personal Computer Memory Card International Association (PCMCIA).

## Slide 9: PCMCIA (contd.)

## Slide 10: Interfacing
An interface is the point of interaction with software, or computer hardware, or with peripheral devices
There are two types of interfaces:
1. Hardware Interfaces.
2. Software Interfaces.

## Slide 11: Interfacing Contd.
HARDWARE INTERFACES: Hardware interfaces exist in computing systems between many of the components such as the various buses, storage devices, other I/O devices, etc.
SOFTWARE INTERFACES: A software interface may refer to a range of different types of interface at different levels.

## Slide 12: Interfacing Contd.
Different levels of software interfacing.
An operating system may interface with pieces of hardware.
Applications or programs running on the operating system may need to interact via streams
In object oriented programs, objects within an application may need to interact via methods.

## Slide 13: Ports
A port serves as an interface between the computer and other computers or peripheral devices
Primarily there are two types of ports:
Physical Ports
Virtual Ports

## Slide 14: Physical Ports:
Physical ports are used for connecting a computer trough a cable and a socket to a peripheral device.
Physical computer ports list includes:
a. Serial ports (DB9 socket)
b. USB ports (USB 2.0 or 3.0 socket / connector)
c. Parallel ports (DB25 socket / connector

## Slide 15: Virtual Ports
Virtual ports are data gates that allow software application (network) to use hardware resources without any interference.
This computer ports (network ports) are defined by IANA (Internet Assigned Numbers Authority).
Used by TCP ( Transmission Control Protocol ), UDP ( User Datagram Protocol ), DCCP ( Datagram Congestion Control Protocol ) and SCTP ( Stream Control Transmission Protocol )

## Slide 16: Storage Devices: Terminology
Medium
  The technology or product type that holds the data
Access Time
  The time to locate data and read it
  Calculated as an average in seconds e.g. - s, ms, µs, ns, etc
Transfer Rate
  Amount of data moves per second
  Calculated in bytes/second e.g. – KBPS, MBPS etc

## Slide 17: Storage Devices: Primary
Primary memory
  Named as cache or conventional memory
  Has an immediate access by the CPU
Expanded storage
  RAM – Random Access Memory
  A buffer between cache memory and secondary memory

## Slide 18: Storage Devices: Secondary
Secondary storage
  Permanent memory
  Non volatile memory
  Data and programs must be copied to primary memory for CPU access
  Electro-Mechanical devices
  Direct access storage devices (DASDs)
  Online storage
  Offline storage – loaded when needed

## Slide 19: Storage Devices: Hierarchy
 | Devices | Access Time | Transfer rate
Primary storage | CPU registers | - | -
 | Cache memory | 15-30 ns | -
 | Conventional memory | 50-100 ns | -
 | Expanded memory | 75-500 ns | -
Secondary storage | Hard disk | 10-50 ms | 600-6000 Kbytes/s
 | Floppy disk | 95 ms | 100-200 Kbytes/s
 | CD-ROM | 100-600 ms | 150-1000 Kbytes/s
 | Tape | 0.5+ s | 200-3000 Kbytes/s

## Slide 20: Storage Devices: Technology
Primary storage
  Semiconductor technology e.g.- RAM
  Volatile i.e. contents are depended on power
Secondary storage
  Magnetic technology e.g. Hard Disk Drives
  Non-volatile i.e. contents are not depended on power

## Slide 21: Storage Devices: Intervention
Online storage
  Storage that is accessible to programs without human intervention
  Primary & Secondary storages are online
  Example- RAM, HDD etc
Offline storage
  Storage that is not accessible to programs without human intervention
  Sometimes called archival storage
  Example- CD, DVD, External HDD etc

## Slide 22: Assignment for next class:
Serial port, Parallel port, USB 10
Relation between peripheral and interfacing 10
Due date: Next lecture day

## Slide 23
Thank you