## Slide 1: 2 bits ALU Peripheral and Interfacing

## Slide 2
What is ALU?
ALU (Arithmetic and Logic Unit) is the part of computer processor that is used for doing arithmetic or logic operation on operands.
What is the basic use of ALU unit?
An arithmetic logic unit (ALU), a memory unit, and input/output(I/O) controllers. The ALU performs simple addition, subtraction, multiplication, division, and logic operations, such as OR and AND. The memory stores the program’s instructions and data.

## Slide 3
2 bit ALU block diagram
2 bit ALU
A0
A1
B1
B0
S0
S1
S2
F0
F1
Cout
Here,
A(A1 A0) = operand
B(B1 B0) = operand
S(S2 S1 S0) = Select inputs
F(F1 F0) = Output
Cout = Carry output

## Slide 4
S2 | S1 | S0 | Output | Function
0 | 0 | 0 | F = A | Transfer A
0 | 0 | 1 | F = A + 1 | Increment A
0 | 1 | 0 | F = A+B | Add B to A
0 | 1 | 1 | F = A+B+1 | Add B to A plus 1
1 | 0 | 0 | F = A + | Add 1’s compliment of B to A
1 | 0 | 1 | F = A + | Add 2’s compliment of B to A
1 | 1 | 0 | F = A-1 | Decrement A
1 | 1 | 1 | F = A | Transfer A
S2 | S1 | S0 | Output | Function
0 | 0 | 0 | F = A | Transfer A
0 | 0 | 1 | F = A + 1 | Increment A
0 | 1 | 0 | F = A+B | Add B to A
0 | 1 | 1 | F = A+B+1 | Add B to A plus 1
1 | 0 | 0 |  | Add 1’s compliment of B to A
1 | 0 | 1 |  | Add 2’s compliment of B to A
1 | 1 | 0 | F = A-1 | Decrement A
1 | 1 | 1 | F = A | Transfer A
Truth Table:

## Slide 5
Now we a going to design the circuit using Proteus. To do so we have to use some pins.
We will use digital pin :
Pin num | Type | Purpose
13 | Output | F0
12 | Output | F1
11 | Output | Cout
10 | Input | A0
9 | Input | A1
8 | Input | B0
7 | Input | B1
6 | Input | S0
5 | Input | S1
4 | Input | S2

## Slide 6
To design this circuit on proteus we will need:
Arduino UNO
LED
Resistor
Switch SPST
Power
ground

## Slide 7
Circuit implementation using Proteus

## Slide 8
Basic Knowledge we will need to implement the code:
Calculate sum and carry with half adder:
sum = A ⊕ B
carry = AB
2. Calculate sum and carry with full adder:
sum = sum = A ⊕ B ⊕ C
carry = AB + BC + CA
3. Calculate difference and borrow with half subtractor:
difference = A ⊕ B
borrow = ĀB
4. Calculate difference and borrow with full subtractor:
difference = A ⊕ B ⊕ C
borrow = BC + Ā(B + C)

## Slide 9
HA
A0
Carry
B1
Sum0
Carry
Cout
FA
B0
A1
F0
F1

## Slide 10
Some operation:
For S2= 0 S1 = 1 S0 = 0 out operation will be A+B
let, A = 1 1 & B = 1 1
Carry = 1 1
A = 1 1
B = 1 1
1 1 0
Here,
For A0 and B0 we use half adder:
Sum (HA) = A0 ⊕ B0 = 1 ⊕ 1=0
Carry (HA)=A0.B0=1.1=1
For A1 and B1 we use full adder , because we get a carry
Sum (FA) = A1 ⊕ B1 ⊕ Carry = 1 ⊕ 1 ⊕ 1=1
Cout (FA) = A1.B1 + B1.Carry + Carry.A1= 1.1 +1.1+1.1=1

## Slide 11
Some operation:
2. For S2= 1 S1 = 0 S0 = 1 out operation will be A +
let, A = 1 1, = 1 0
Carry = 1 1
A = 1 1
B = 1 0
1
1 1 0
Here,
For A0 and B0 we use full adder:
Sum (HA) = A0 ⊕ B0 ⊕ 1= 1 ⊕ 0 ⊕ 1=0
Carry (HA)=A0.B0 + B0.1 + 1.A0 = 1.0 + 0.1 + 1.1 = 1
For A1 and B1 we use full adder , because we get a carry
Sum (FA) = A1 ⊕ B1 ⊕ Carry = 1 ⊕ 1 ⊕ 1 = 1
Cout (FA) = A1.B1 + B1.Carry + Carry.A1 = 1.1+1.1+1.1 =1

## Slide 12
Code:

## Slide 17
THANK YOU