## Slide 1: Sonar Sensor with the Implementation
CSE 315
Peripherals & Interfacing

## Slide 2
What is Sonar?
Sonar is a technique that uses sound propagation to navigate, communicate with or detect objects on or under the surface of the water.

## Slide 3
Ultrasonic Sensor
An Ultrasonic sensor is a device that can measure the distance to an object by using sound waves.

## Slide 4: Pin Configuration
VCC
The Vcc pin powers the sensor, typically with +5V
Trig
Trigger pin is an Input pin. This pin has to be kept high for 10us to initialize measurement by sending US wave.
Echo
Echo pin is an Output pin. This pin goes high for a period of time which will be equal to the time taken for the US wave to return back to the sensor.
GND
This pin is connected to the Ground of the system.

## Slide 5: Features:
Operating voltage: +5V
Theoretical Measuring Distance: 2cm to 450cm
Practical Measuring Distance: 2cm to 80cm
Accuracy: 3mm
Measuring angle covered: <15°
Operating Current: <15mA
Operating Frequency: 40Hz
Trigger Input Pulse width: 10uS

## Slide 6
The transmitter (trig pin) sends a signal: a high-frequency sound.
1
When the signal finds an object, it is reflected and back toward the sensor
2
And the receiver(echo pin) receives/observed it.
3
Working principle

## Slide 7
Obstacles finding robots
Smart (gloves, white cane, shoe, hat) etc.
Mapping
biped robot, obstacle avoider robot, path finding robot etc.
Liquid Level Sensing
Water Depth Sensing with Ultrasonic and Wastewater Management
Product for Blind people
Easy Control of Trash Collection Vehicles
Vehicle Detection
Car Washes,
Automotive Assembly, and Parking Garage Applications
Applications
150 ultrasonic projects
https://www.hackster.io/projects/tags/ultrasonic

## Slide 8: Contd…

## Slide 9: Contd….
Intelligent self balance robot
Smart White Cane
Wall follower robot
Trash level detection
Car parking

## Slide 10: Diagram :

## Slide 11: Code:
const int trigPin = 13;
const int echoPin = 12;
const int led = 11;
void setup()
{ Serial.begin (9600);
pinMode(trigPin, OUTPUT);
pinMode(echoPin, INPUT);
pinMode(led, OUTPUT);
}
void loop()
{
long duration, distance;
digitalWrite(trigPin, LOW);
delayMicroseconds(2);
digitalWrite(trigPin, HIGH);
delayMicroseconds(10);
digitalWrite(trigPin, LOW);
duration = pulseIn(echoPin, HIGH);
distance = (duration/2) * 0.034;
if (distance < 10)
{
digitalWrite(led,HIGH);
}
else {
digitalWrite(led,LOW);
}
}

## Slide 12: Distance= velocity * time
s= 343 m/s * (duration/2) [As the duration of time has been calculated for two ways]
s= 34300 cm/s * (duration/2)
s= 34300/1000000 cm/micro-sec * (duration/2)
s= 0.0343 cm/us * (duration/2)

## Slide 13: Hardware Requirements (Proteus)
Arduino
LED
Pot & Pot HG
Ultrasonic V2.0 B

## Slide 14: Library for Proteus
Put the following in the path:
C>Program data>Labcenterelectronics>Proteus8Professional>Library
Files name:
1. UltrasonicTEP.HEX
2. UltrasonicTEP
3. UltrasonicTEP.LIB

## Slide 15: Proteus integration

## Slide 16: Proteus integration

## Slide 17: Proteus integration

## Slide 18: Library Path
C:\ProgramData\Labcenter Electronics\Proteus 8 Professional\LIBRARY\UltrasonicTEP.HEX

## Slide 19: Proteus integration (working)

## Slide 20: Proteus integration (working)-value less than 10

## Slide 21
pulseIn():Reads the echoPin, returns the sound wave travel time in microseconds. if value is HIGH, pulseIn() waits for the pin to go HIGH, starts timing
Distance = Speed × Time ; here universal speed of US wave at room conditions is 340m/s. convert to 0.034 cm/us.
Duration: divide the duration by 2 because the wave was sent, hit the object, and then returned back to the sensor.

## Slide 22
THANK YOU