## Slide 1: COD Ch. 7 Large and Fast: Exploiting Memory Hierarchy

## Slide 2: Memories: Review
DRAM (Dynamic Random Access Memory):
  value is stored as a charge on capacitor that must be periodically refreshed, which is why it is called dynamic
  very small – 1 transistor per bit – but factor of 5 to 10 slower than SRAM
  used for main memory
SRAM (Static Random Access Memory):
  value is stored on a pair of inverting gates that will exist indefinitely as long as there is power, which is why it is called static
  very fast but takes up more space than DRAM – 4 to 6 transistors per bit
  used for cache

## Slide 3: Memory Hierarchy
Users want large and fast memories…
  expensive and they don’t like to pay…
Make it seem like they have what they want…
  memory hierarchy
  hierarchy is inclusive, every level is subset of lower level
  performance depends on hit rates
Block of data
(unit of data copy)

## Slide 4: Locality
Locality is a principle that makes having a memory hierarchy a good idea
If an item is referenced then because of
  temporal locality: it will tend to be again referenced soon
  spatial locality: nearby items will tend to be referenced soon
  why does code have locality – consider instruction and data?

## Slide 5: Hit and Miss
Focus on any two adjacent levels – called, upper (closer to CPU) and lower (farther from CPU) – in the memory hierarchy, because each block copy is always between two adjacent levels
Terminology:
  block: minimum unit of data to move between levels
  hit: data requested is in upper level
  miss: data requested is not in upper level
  hit rate: fraction of memory accesses that are hits (i.e., found at upper level)
  miss rate: fraction of memory accesses that are not hits
    miss rate = 1 – hit rate
  hit time: time to determine if the access is indeed a hit + time to access and deliver the data from the upper level to the CPU
  miss penalty: time to determine if the access is a miss + time to replace block at upper level with corresponding block at lower level + time to deliver the block to the CPU

## Slide 6: Caches
By simple example
  assume block size = one word of data
Issues:
  how do we know if a data item is in the cache?
  if it is, how do we find it?
  if not, what do we do?
Solution depends on cache addressing scheme…
Reference to Xn
causes miss so
it is fetched from
memory

## Slide 7: Direct Mapped Cache
Addressing scheme in direct mapped cache:
  cache block address = memory block address mod cache size (unique)
  if cache size = 2m, cache address = lower m bits of n-bit memory address
  remaining upper n-m bits kept kept as tag bits at each cache block
  also need a valid bit to
  recognize valid entry

## Slide 8: Accessing Cache
Example:
Index V Tag Data
000 N
001 N
010 N
011 N
100 N
101 N
110 N
111 N
Index V Tag Data
000 N
001 N
010 N
011 N
100 N
101 N
110 Y 10 Mem(10110)
111 N
(0) Initial state:
(1) Address referred 10110 (miss):

## Slide 9
Index V Tag Data
000 N
001 N
010 Y 11 Mem(11010)
011 N
100 N
101 N
110 Y 10 Mem(10110)
111 N
(2) Address referred 11010 (miss):
Index V Tag Data
000 N
001 N
010 Y 11 Mem(11010)
011 N
100 N
101 N
110 Y 10 Mem(10110)
111 N
(3) Address referred 10110 (hit):
Index V Tag Data
000 N
001 N
010 Y 10 Mem(10010)
011 N
100 N
101 N
110 Y 10 Mem(10110)
111 N
(4) Address referred 10010 (miss):
to CPU

## Slide 10: Direct Mapped Cache
MIPS style:
What kind of locality are we taking advantage of?
Address showing bit positions
Cache with 1024 1-word blocks: byte offset
(least 2 significant bits) is ignored and
next 10 bits used to index into cache

## Slide 11: Cache Read Hit/Miss
Cache read hit: no action needed
Instruction cache read miss:
  Send original PC value (current PC – 4, as PC has already been incremented in first step of instruction cycle) to memory
  Instruct main memory to perform read and wait for memory to complete access – stall on read
  After read completes write cache entry
  Restart instruction execution at first step to refetch instruction
Data cache read miss:
  Similar to instruction cache miss
  To reduce data miss penalty allow processor to execute instructions while waiting for the read to complete until the word is required – stall on use (why won’t this work for instruction misses?)

## Slide 12: DECStation 3100 Cache (MIPS R2000 processor)
Address showing bit positions
Cache with 16K 1-word blocks: byte offset
(least 2 significant bits) is ignored and
next 14 bits used to index into cache

## Slide 13: Cache Write Hit/Miss
Write-through scheme
  on write hit: replace data in cache and memory with every write hit to avoid inconsistency
  on write miss: write the word into cache and memory – obviously no need to read missed word from memory!
  Write-through is slow because of always required memory write
    performance is improved with a write buffer where words are stored while waiting to be written to memory – processor can continue execution until write buffer is full
    when a word in the write buffer completes writing into main that buffer slot is freed and becomes available for future writes
    DEC 3100 write buffer has 4 words
Write-back scheme
  write the data block only into the cache and write-back the block to main only when it is replaced in cache
  more efficient than write-through, more complex to implement

## Slide 14: Direct Mapped Cache: Taking Advantage of Spatial Locality
Taking advantage of spatial locality with larger blocks:
Address showing bit positions
Cache with 4K 4-word blocks: byte offset (least 2 significant bits) is ignored, next 2 bits are block offset, and the next 12 bits are used to index into cache

## Slide 15: Direct Mapped Cache: Taking Advantage of Spatial Locality
Cache replacement in large (multiword) blocks:
  word read miss: read entire block from main memory
  word write miss: cannot simply write word and tag! Why?!
  writing in a write-through cache:
    if write hit, i.e., tag of requested address and and cache entry are equal, continue as for 1-word blocks by replacing word and writing block to both cache and memory
    if write miss, i.e., tags are unequal, fetch block from memory, replace word that caused miss, and write block to both cache and memory
    therefore, unlike case of 1-word blocks, a write miss with a multiword block causes a memory read

## Slide 16: Direct Mapped Cache: Taking Advantage of Spatial Locality
Miss rate falls at first with increasing block size as expected, but, as block size becomes a large fraction of total cache size, miss rate may go up because
  there are few blocks
  competition for blocks increases
  blocks get ejected before most of their words are accessed (thrashing in cache)
Miss rate vs. block size for
various cache sizes

## Slide 17: Example Problem
How many total bits are required for a direct-mapped cache with 128 KB of data and 1-word block size, assuming a 32-bit address?
Cache data = 128 KB = 217 bytes = 215 words = 215 blocks
Cache entry size = block data bits + tag bits + valid bit
= 32 + (32 – 15 – 2) + 1 = 48 bits
Therefore, cache size = 215  48 bits = 215  (1.5  32) bits = 1.5  220 bits = 1.5 Mbits
  data bits in cache = 128 KB  8 = 1 Mbits
  total cache size/actual cache data = 1.5

## Slide 18: Example Problem
How many total bits are required for a direct-mapped cache with 128 KB of data and 4-word block size, assuming a 32-bit address?
Cache size = 128 KB = 217 bytes = 215 words = 213 blocks
Cache entry size = block data bits + tag bits + valid bit
= 128 + (32 – 13 – 2 – 2) + 1 = 144 bits
Therefore, cache size = 213  144 bits = 213  (1.25  128) bits = 1.25  220 bits = 1.25 Mbits
  data bits in cache = 128 KB  8 = 1 Mbits
  total cache size/actual cache data = 1.25

## Slide 19: Example Problem
Consider a cache with 64 blocks and a block size of 16 bytes. What block number does byte address 1200 map to?
As block size = 16 bytes:
byte address 1200  block address 1200/16  = 75
As cache size = 64 blocks:
block address 75  cache block (75 mod 64) = 11

## Slide 20: Improving Cache Performance
Use split caches for instruction and data because there is more spatial locality in instruction references:
Make reading multiple words (higher bandwidth) possible by increasing physical or logical width of the system…
Miss rates for gcc and spice in a MIPS R2000
with one and four word block sizes

## Slide 21: Improving Cache Performance by Increasing Bandwidth
Assume:
  cache block of 4 words
  1 clock cycle to send address to memory address buffer (1 bus trip)
  15 clock cycles for each memory data access
  1 clock cycle to send data to memory data buffer (1 bus trip)
Miss penalties
1 + 4*15 + 4*1 = 65 cycles
1 + 1*15 +1*1 = 17 cycles
4 word wide memory and bus
1 +1*15 + 4*1 = 20 cycles
4 word wide memory only
Proce-
ssor
Memory
bank 0
Memory
bank 2
Memory
bank 3
Memory
bank 1
Bus
Interleaved memory units
compete for bus

## Slide 22: Performance
Simplified model assuming equal read and write miss penalties:
  CPU time = (execution cycles + memory stall cycles) ´ cycle time
  memory stall cycles = memory accesses ´ miss rate ´ miss penalty
Therefore, two ways to improve performance in cache:
  decrease miss rate
  decrease miss penalty
  what happens if we increase block size?

## Slide 23: Example Problems
Assume for a given machine and program:
  instruction cache miss rate 2%
  data cache miss rate 4%
  miss penalty always 40 cycles
  CPI of 2 without memory stalls
  frequency of load/stores 36% of instructions
How much faster is a machine with a perfect cache that never misses?
What happens if we speed up the machine by reducing its CPI to 1 without changing the clock rate?
What happens if we speed up the machine by doubling its clock rate, but if the absolute time for a miss penalty remains same?

## Slide 24: Solution
1.
Assume instruction count = I
Instruction miss cycles = I  2%  40 = 0.8  I
Data miss cycles = I  36%  4%  40 = 0.576  I
So, total memory-stall cycles = 0.8  I + 0.576  I = 1.376  I
  in other words, 1.376 stall cycles per instruction
Therefore, CPI with memory stalls = 2 + 1.376 = 3.376
Assuming instruction count and clock rate remain same for a perfect cache and a cache that misses:
CPU time with stalls / CPU time with perfect cache
= 3.376 / 2 = 1.688
Performance with a perfect cache is better by a factor of 1.688

## Slide 25: Solution (cont.)
2.
CPI without stall = 1
CPI with stall = 1 + 1.376 = 2.376 (clock has not changed so stall cycles per instruction remains same)
CPU time with stalls / CPU time with perfect cache
= CPI with stall / CPI without stall
= 2.376
Performance with a perfect cache is better by a factor of 2.376
Conclusion: with higher CPI cache misses “hurt more” than with lower CPI

## Slide 26: Solution (cont.)
3.
With doubled clock rate, miss penalty = 2  40 = 80 clock cycles
Stall cycles per instruction = (I  2%  80) + (I  36%  4%  80)
= 2.752  I
So, faster machine with cache miss has CPI = 2 + 2.752 = 4.752
CPU time with stalls / CPU time with perfect cache
= CPI with stall / CPI without stall
= 4.752 / 2 = 2.376
Performance with a perfect cache is better by a factor of 2.376
Conclusion: with higher clock rate cache misses “hurt more” than with lower clock rate

## Slide 27: Decreasing Miss Rates with Associative Block Placment
Direct mapped: one unique cache location for each memory block
  cache block address = memory block address mod cache size
Fully associative: each memory block can locate anywhere in cache
  all cache entries are searched (in parallel) to locate block
Set associative: each memory block can place in a unique set of cache locations – if the set is of size n it is n-way set-associative
  cache set address = memory block address mod number of sets in cache
  all cache entries in the corresponding set are searched (in parallel) to locate block
Increasing degree of associativity
  reduces miss rate
  increases hit time because of the parallel search and then fetch

## Slide 28: Decreasing Miss Rates with Associative Block Placment
Direct Mapped
2-way Set Associative
Fully Associative
Location of a memory block with address 12 in a cache with 8 blocks
with different degrees of associativity
12 mod 8 = 4
12 mod 4 = 0

## Slide 29: Decreasing Miss Rates with Associative Block Placment
One-way set associative
Configurations of an 8-block cache with different degrees of associativity

## Slide 30: Example Problems
Find the number of misses for a cache with four 1-word blocks given the following sequence of memory block accesses: 0, 8, 0, 6, 8, for each of the following cache configurations
  direct mapped
  2-way set associative (use LRU replacement policy)
  fully associative
Note about LRU replacement
  in a 2-way set associative cache LRU replacement can be implemented with one bit at each set whose value indicates the mostly recently referenced block

## Slide 31: Solution
1 (direct-mapped)
5 misses
Block address Cache block
0 0 (= 0 mod 4)
6 2 (= 6 mod 4)
8 0 (= 8 mod 4)
Address of memory Hit or Contents of cache blocks after reference
block accessed miss 0 1 2 3
0 miss Memory[0]
8 miss Memory[8]
0 miss Memory[0]
6 miss Memory[0] Memory[6]
8 miss Memory[8] Memory[6]
Block address translation in direct-mapped cache
Cache contents after each reference – red indicates new entry added

## Slide 32: Solution (cont.)
2 (two-way set-associative)
Four misses
Block address Cache set
0 0 (= 0 mod 2)
6 0 (= 6 mod 2)
8 0 (= 8 mod 2)
Address of memory Hit or Contents of cache blocks after reference
block accessed miss Set 0 Set 0 Set 1 Set 1
0 miss Memory[0]
8 miss Memory[0] Memory[8]
0 hit Memory[0] Memory[8]
6 miss Memory[0] Memory[6]
8 miss Memory[8] Memory[6]
Block address translation in a two-way set-associative cache
Cache contents after each reference – red indicates new entry added

## Slide 33: Solution (cont.)
3 (fully associative)
3 misses
Address of memory Hit or Contents of cache blocks after reference
block accessed miss Block 0 Block 1 Block 2 Block 3
0 miss Memory[0]
8 miss Memory[0] Memory[8]
0 hit Memory[0] Memory[8]
6 miss Memory[0] Memory[8] Memory[6]
8 hit Memory[0] Memory[8] Memory[6]
Cache contents after each reference – red indicates new entry added

## Slide 34: Implementation of a Set-Associative Cache
Address
4-way set-associative cache with 4 comparators and one 4-to-1 multiplexor:
size of cache is 1K blocks = 256 sets * 4-block set size
Set