## Slide 1: CSE 317 Lecture 2
Computer performance

## Slide 2: The Computer Revolution
Progress in computer technology .
Makes novel applications feasible.
  Computer in Automobile.
  Cell phone
  Worldwide web
  Search engine …..etc.

## Slide 3: Performance
Performance is the key to understanding underlying motivation for the hardware and its organization
Measure, report, and summarize performance to enable users to
  make intelligent choices
  see through the marketing hype!
Why is some hardware better than others for different programs?
What factors of system performance are hardware related? (e.g., do we need a new machine, or a new operating system?)
How does the machine's instruction set affect performance?
Notes: 3

## Slide 4: The Role of Performance
Response Time
Throughput
Relative performance
Measuring Execution time
CPU time
CPU clocking ,instruction count and CPI

## Slide 5: What do we measure? Define performance….
Airplane Passengers Range (mi) Speed (mph)
Boeing 737-100 101 630 598
Boeing 747 470 4150 610
BAC/Sud Concorde 132 4000 1350
Douglas DC-8-50 146 8720 544
How much faster is the Concorde compared to the 747?
How much bigger is the Boeing 747 than the Douglas DC-8?
So which of these airplanes has the best performance?!
Notes: 5

## Slide 6: Computer Performance: TIME, TIME, TIME!!!
Response Time (elapsed time, latency):
  how long does it take for my job to run?
  how long does it take to execute (start to
  finish) my job?
  how long must I wait for the database query?
Throughput:
  how many jobs can the machine run at once?
  what is the average execution rate?
  how much work is getting done?
If we upgrade a machine with a new processor what do we increase?
If we add a new machine to the lab what do we increase?
Individual user
concerns…
Systems manager
concerns…
Notes: 6
Have them raise their hands when answering questions

## Slide 7: Execution Time
Elapsed Time
  counts everything (disk and memory accesses, waiting for I/O, running other programs, etc.) from start to finish
  a useful number, but often not good for comparison purposes
elapsed time = CPU time + wait time (I/O, other programs, etc.)
CPU time
  doesn't count waiting for I/O or time spent running other programs
  can be divided into user CPU time and system CPU time (OS calls)
CPU time = user CPU time + system CPU time
⇒ elapsed time = user CPU time + system CPU time + wait time
Our focus: user CPU time (CPU execution time or, simply, execution time)
  time spent executing the lines of code that are in our program
Notes: 7

## Slide 8: Definition of Performance
For some program running on machine X: PerformanceX = 1 / Execution timeX This means that for two computers X and Y, if the performance of X is greater than the performance of Y,
We have
PerformanceX > PerformanceY
1/ execution of time X > 1/ execution time of Y
Execution timeY > Execution timeX
X is n times faster than Y means: PerformanceX / PerformanceY = n
Notes: 8

## Slide 9: Example of Relative performance
If Afia’s Computer runs a program in 10 seconds and Tahmid’s computer runs the same program in 15 seconds, whose computer is faster and by how much faster?

## Slide 10: Clock Cycles
Instead of reporting execution time in seconds, we often use cycles. In modern computers hardware events progress cycle by cycle: in other words, each event, e.g., multiplication, addition, etc., is a sequence of cycles
Clock ticks indicate start and end of cycles:
cycle time = time between ticks = seconds per cycle
clock rate (frequency) = cycles per second (1 Hz. = 1 cycle/sec, 1 MHz. = 106 cycles/sec)
Example: A 200 Mhz. clock has a cycle time
time
cycle
tick
tick
Notes: 10

## Slide 11: Performance Equation I
So, to improve performance one can either:
  reduce the number of cycles for a program, or
  reduce the clock cycle time, or, equivalently,
  increase the clock rate
CPU execution time CPU clock cycles Clock cycle time
for a program for a program
=
×
equivalently

## Slide 12: How many cycles are required for a program?
Could assume that # of cycles = # of instructions
time
1st instruction
2nd instruction
3rd instruction
4th
5th
6th
...
This assumption is incorrect! Because:
  Different instructions take different amounts of time (cycles)
  Why…?
Notes: 12

## Slide 13: How many cycles are required for a program?
Multiplication takes more time than addition
Floating point operations take longer than integer ones
Accessing memory takes more time than accessing registers
Important point: changing the cycle time often changes the number of cycles required for various instructions because it means changing the hardware design. More later…
time
Notes: 13

## Slide 14: Example
Our favorite program runs in 10 seconds on computer A, which has a 400Mhz. clock.
We are trying to help a computer designer build a new machine B, that will run this program in 6 seconds. The designer can use new (or perhaps more expensive) technology to substantially increase the clock rate, but has informed us that this increase will affect the rest of the CPU design, causing machine B to require 1.2 times as many clock cycles as machine A for the same program.
What clock rate should we tell the designer to target?
Notes: 14

## Slide 15: Terminology
A given program will require:
  some number of instructions (machine instructions)
  some number of cycles
  some number of seconds
We have a vocabulary that relates these quantities:
  cycle time (seconds per cycle)
  clock rate (cycles per second)
  (average) CPI (cycles per instruction)
    a floating point intensive application might have a higher average CPI
  MIPS (millions of instructions per second)
    this would be higher for a program using simple instructions
Notes: 15

## Slide 16: Performance Measure
Performance is determined by execution time
Do any of these other variables equal performance?
  # of cycles to execute program?
  # of instructions in program?
  # of cycles per second?
  average # of cycles per instruction?
  average # of instructions per second?
Common pitfall : thinking one of the variables is indicative of performance when it really isn’t
Notes: 16

## Slide 17: Performance Equation II
CPU execution time Instruction count average CPI Clock cycle time
for a program for a program
Derive the above equation from Performance Equation I
=
×
×

## Slide 18: CPI Example I
Suppose we have two implementations of the same instruction set architecture (ISA). For some program:
  machine A has a clock cycle time of 10 ns. and a CPI of 2.0
  machine B has a clock cycle time of 20 ns. and a CPI of 1.2
Which machine is faster for this program, and by how much?
If two machines have the same ISA, which of our quantities (e.g., clock rate, CPI, execution time, # of instructions, MIPS) will always be identical?
Notes: 18

## Slide 19: CPI Example II
A compiler designer is trying to decide between two code sequences for a particular machine.
Based on the hardware implementation, there are three different classes of instructions: Class A, Class B, and Class C, and they require 1, 2 and 3 cycles (respectively).
The first code sequence has 5 instructions:
2 of A, 1 of B, and 2 of C The second sequence has 6 instructions:
4 of A, 1 of B, and 1 of C.
Which sequence will be faster? How much? What is the CPI for each sequence?
Notes: 19

## Slide 20: MIPS Example
Two different compilers are being tested for a 500 MHz. machine with three different classes of instructions: Class A, Class B, and Class C, which require 1, 2 and 3 cycles (respectively). Both compilers are used to produce code for a large piece of software.
Compiler 1 generates code with 5 billion Class A instructions, 1 billion Class B instructions, and 1 billion Class C instructions.
Compiler 2 generates code with 10 billion Class A instructions, 1 billion Class B instructions, and 1 billion Class C instructions.
Which sequence will be faster according to MIPS?
Which sequence will be faster according to execution time?
Notes: 20

## Slide 21: Benchmarks
Performance best determined by running a real application
  use programs typical of expected workload
  or, typical of expected class of applications e.g., compilers/editors, scientific applications, graphics, etc.
Small benchmarks
  nice for architects and designers
  easy to standardize
  can be abused!
Benchmark suites
  Perfect Club: set of application codes
  Livermore Loops: 24 loop kernels
  Linpack: linear algebra package
  SPEC: mix of code from industry organization
Notes: 21

## Slide 22: Summary
Performance is specific to a particular program
  total execution time is a consistent summary of performance
For a given architecture performance increases come from:
  increases in clock rate (without adverse CPI affects)
  improvements in processor organization that lower CPI
  compiler enhancements that lower CPI and/or instruction count
Pitfall: expecting improvement in one aspect of a machine’s performance to affect the total performance
Notes: 22