## Slide 1
Signal Strength
The strength of a signal is measured by how closely it approximates an ideal voltage source.
  VDD and GND rails are strongest 1 and 0
  nMOS pass strong 0
    But degraded or weak 1
  pMOS pass strong 1
    But degraded or weak 0
  Thus nMOS are best for pull-down network

## Slide 2
When a transistor is used as switch
We get a pass transistor
Pass Transistors
28-Feb-21
2

## Slide 3
Pass transistors produce degraded outputs
Transmission gates pass both 0 and 1 well
Transmission Gates

## Slide 4
Tri-state
Digital Buffer Circuit
Known as 3-state Buffer or Tri-state Buffer
An external “Control” or “Enable” ( EN ) controls the input
When Enable is ON, Input goes to Output
Otherwise, a floating Z state is obtained at the Output
A tri-state buffer requires two inputs. One being the data input and the other being the enable or control input

## Slide 5
Tristate buffer produces Z when not enabled
EN | A | Y
0 | 0 | Z
0 | 1 | Z
1 | 0 | 0
1 | 1 | 1
Tri-state

## Slide 6
Transmission gate acts as tristate buffer
  only requires two transistors but it is a non restoring circuit
  If the input is noisy or otherwise degraded, the output will receive the same noise
Non-restoring Tri-state
EN | A | Y
0 | 0 | Z
0 | 1 | Z
1 | 0 | 0
1 | 1 | 1

## Slide 7
Tristate inverter produces restored output
  Violates conduction complement rule
  Because we want a Z output
Tri-state Inverter

## Slide 8
Multiplexers (MUX)
The multiplexer is a combinational logic circuit designed to switch one of several input lines to a single common output line.
Multiplexers are key components in CMOS memory elements and data manipulation structures.
2:1 multiplexer chooses between two inputs

## Slide 9
Multiplexer truth table

## Slide 10
Non-restoring mux uses two transmission gates
  Only 4 transistors
Transmission Gate Mux

## Slide 11
Inverting multiplexer
  Use compound AOI22
  Or a pair of tristate inverters
  Essentially the same thing
Noninverting multiplexer adds an inverter
Inverting Mux

## Slide 12
4:1 Multiplexer
4:1 mux chooses one of 4 inputs using two selects
  Two levels of 2:1 muxes
  Or four tristates

## Slide 13
4:1 Multiplexer
The Boolean expression for this 4-to-1 Multiplexer above with inputs A to D and data select lines a, b is given as:

## Slide 14
4:1 Multiplexer using OR gate

## Slide 15
Sequential circuit
A sequential circuit is a logical circuit, where the output depends on the present value of the input signal as well as the sequence of past inputs.
Example: latches , ﬂip-ﬂops

## Slide 16
The data latch is an easy expansion to the gated SR-latch that eliminates the chance of unacceptable states of input.
D latch is built from a 2-input multiplexer and two inverters.
The multiplexer is built from a pair of transmission gates
D Latch

## Slide 17
When CLK = 1, the latch is transparent and D ﬂows through to Q.
When CLK falls to 0, the latch becomes opaque. A feedback path around the inverter pair is established to hold the current state of Q indeﬁnitely.
D Latch Operation

## Slide 18
Also known as a level-sensitive latch because the state of the output is dependent on the level of the clock signal
D Latch Operation

## Slide 19
D-Flip-flop
By combining two level-sensitive latches, one negative-sensitive and one positive-sensitive, we construct the edge-triggered ﬂip-ﬂop.
The ﬁrst latch stage is called the master and the second is called the slave.

## Slide 20
D Flip-flop
While CLK is low, the master negative-level-sensitive latch output (QM) follows the D input while the slave positive-level-sensitive latch holds the previous value.

## Slide 21
D Flip-flop
When the clock transitions from 0 to 1, the master latch becomes opaque and holds the D value at the time of the clock transition.
The slave latch becomes transparent, passing the stored master value (QM) to the output of the slave latch (Q).
The D input is blocked from affecting the output because the master is disconnected from the D.

## Slide 22
D Flip-flop
D flip-flop is called a positive-edge triggered ﬂip-ﬂop.
Also called a D ﬂip-ﬂop, D register, or master–slave ﬂip-ﬂop.
A collection of D ﬂip-ﬂops sharing a common clock input is called a register.
A register is often drawn as a ﬂip-ﬂop with multi-bit D and Q busses.