## Slide 1: Chapter 4. Digital Transmission
Digital-to-Digital Conversion
Analog-to-Digital Conversion
Transmission Mode

## Slide 2: Digital-to-Digital Conversion
Involves three techniques:
  Line coding (always needed), block coding, and scrambling
Line coding: the process of converting digital data to digital signals
3-2

## Slide 3: Signal Element and Data Element
Data elements are what we need to send; signal elements are what we can send
3-3

## Slide 4: Data Rate Versus Signal Rate
Data rate defines the number of data elements (bits) sent in 1s: bps
Signal rate is the number of signal elements sent in 1s: baud
Data rate = bit rate, signal rate = pulse rate, modulation rate, baud rate
S = c x N x 1/r, where N is the date rate; c is the case factor, S is the number of signal elements; r is the number of data elements carried by each signal element
Although the actual bandwidth of a digital signal is infinite, the effective bandwidth is finite
The bandwidth is proportional to the signal rate (baud rate)
The minimum bandwidth: Bmin = c x N x 1/r
The maximum data rate: Nmax = 1/c x B x r
3-4

## Slide 5: Design Consideration for Line Coding Scheme
Baseline wandering
  Long string of 0s and 1s can cause a drift in the baseline
DC components
  DC or low frequencies cannot pass a transformer or telephone line (below 200 Hz)
Self-synchronization
Built-in error detection
Immunity to noise and interference
Complexity
3-5

## Slide 6: Lack of Synchronization
3-6

## Slide 7: Line Coding Schemes
3-7

## Slide 8: Unipolar Scheme
One polarity: one level of signal voltage
Unipolar NRZ (None-Return-to-Zero) is simple, but
  DC component : Cannot travel through microwave or transformer
  Synchronization : Consecutive 0’s and 1’s are hard to be synchronized  Separate line for a clock pulse
  Normalized power is double that for polar NRZ
3-8

## Slide 9: Polar Scheme
Two polarity: two levels of voltage
Problem of DC component is alleviated (NRZ,RZ) or eliminated (Biphaze)
3-9

## Slide 10: Polar NRZ
NRZ-L (Non Return to Zero-Level)
  Level of the voltage determines the value of the bit
NRZ-I (Non Return to Zero-Invert)
  Inversion or the lack of inversion determines the value of the bit
3-10

## Slide 11: Polar NRZ: NRZ-L and NRZ-I
Baseline wandering problem
  Both, but NRZ-L is twice severe
Synchronization Problem
  Both, but NRZ-L is more serious
NRZ-L and NRZ-I both have an average signal rate of N/2 Bd
Both have a DC component problem
3-11

## Slide 12: RZ
Provides synchronization for consecutive 0s/1s
Signal changes during each bit
Three values (+, -, 0) are used
  Bit 1: positive-to-zero transition, bit 0: negative-to-zero transition
3-12

## Slide 13: Biphase
Combination of RZ and NRZ-L ideas
Signal transition at the middle of the bit is used for synchronization
Manchester
  Used for Ethernet LAN
  Bit 1: negative-to-positive transition
  Bit 0: positive-to-negative transition
Differential Manchester
  Used for Token-ring LAN
  Bit 1: no transition at the beginning of a bit
  Bit 0: transition at the beginning of a bit
3-13

## Slide 14: Polar Biphase
Minimum bandwidth is 2 times that of NRZ
3-14

## Slide 15: Bipolar Scheme
Three levels of voltage, called “multilevel binary”
Bit 0: zero voltage, bit 1: alternating +1/-1
  (Note) In RZ, zero voltage has no meaning
AMI (Alternate Mark Inversion) and pseudoternary
  Alternative to NRZ with the same signal rate and no DC component problem
3-15

## Slide 16: Multilevel Scheme
To increase the number of bits per baud by encoding a pattern of m data elements into a pattern of n signal elements
In mBnL schemes, a pattern of m data elements is encoded as a pattern of n signal elements in which 2m ≤ Ln
2B1Q (two binary, one quaternary)
8B6T (eight binary, six ternary)
4D-PAM5 (four-dimensional five-level pulse amplitude modulation)
3-16

## Slide 17: 2B1Q: for DSL
3-17

## Slide 18: Summary of Line Coding Schemes
3-18

## Slide 19: Block Coding
Block coding is normally referred to as mB/nB coding; it replaces each m-bit group with an n-bit group
3-19

## Slide 20: 4B/5B
Solve the synchronization problem of NRZ-I
20% increase the signal rate of NRZ-I (Biphase scheme has the signal rate of 2 times that of NRZ-I
Still DC component problem
3-20

## Slide 21: 4B/5B Mapping Codes
3-21

## Slide 22: 8B/10B
210 – 28 = 768 redundant groups used for disparity checking and error detection
3-22

## Slide 23: Scrambling
Biphase : not suitable for long distance communication due to its wide bandwidth requirement
Combination of block coding and NRZ: not suitable for long distance encoding due to its DC component problem
Bipolar AMI: synchronization problem  Scrambling
3-23

## Slide 24: B8ZS
Commonly used in North America
Updated version of AMI with synchronization
Substitutes eight consecutive zeros with 000VB0VB
V denotes “violation”, B denotes “bipolar”
3-24

## Slide 25: HDB3
High-density bipolar 3-zero
Commonly used outside of North America
HDB3 substitutes four consecutive zeros with 000V or B00V depending on the number of nonzero pulses after the last substitution
3-25

## Slide 26: Sampling: Analog-to-Digital Conversion
Analog information (e.g., voice)  digital signal (e.g., 10001011…)
Codec(Coder/Decoder): A/D converter
3-26

## Slide 27: PCM
Pulse Code Modulation
Three processes
  The analog signal is sampled
  The sampled signal is quantized
  The quantized values are encoded as streams of bits
Sampling: PAM (Pulse amplitude Modulation)
  According to the Nyquist theorem, the sampling rate must be at least 2 times the highest frequency contained in the signal.
3-27

## Slide 28: Components of PCM Encoder
3-28

## Slide 29: Different Sampling Methods for PCM
3-29

## Slide 30: Quantization
3-30
Dr. Md. Abdur Razzaque
Green Networking Research Group
Dept. of Computer Science and Engineering, University of Dhaka

## Slide 31: Quantization
Quantization level (L)
Quantization error : depending on L (or nb )
  SNRdB = 6.02nb + 1.76 dB
Nonuniform quantization:
  Companding and expanding
  Effectively reduce the SNRdB
3-31

## Slide 32: Delta Modulation
To reduce the complexity of PCM
3-32

## Slide 33: Delta Modulation Components
3-33

## Slide 34: Delta Demodulation Components
3-34

## Slide 35: Transmission Modes
3-35

## Slide 36: Parallel Transmission
Use n wires to send n bits at one time synchronously
Advantage: speed
Disadvantage: cost  Limited to short distances
3-36

## Slide 37: Serial Transmission
On communication channel
Advantage: reduced cost
Parallel/serial converter is required
Three ways: asynchronous, synchronous, or isochronous
3-37

## Slide 38: Asynchronous Transmission
Use start bit (0) and stop bits (1s)
A gap between two bytes: idle state or stop bits
It means asynchronous at byte level
Must still be synchronized at bit level
Good for low-speed communications (terminal)
3-38

## Slide 39: Synchronous Transmission
Bit stream is combined into “frames”
Special sequence of 1/0 between frames: No gap
Timing is important in midstream
Byte synchronization in the data link layer
Advantage: speed  high-speed transmission
3-39