## Slide 1: Operational Amplifiers
or Op Amps for short

## Slide 2: Op Amps Applications
Audio amplifiers
  Speakers and microphone circuits in cell phones, computers, mpg players, boom boxes, etc.
Instrumentation amplifiers
  Biomedical systems including heart monitors and oxygen sensors.
Power amplifiers
Analog computers
  Combination of integrators, differentiators, summing amplifiers, and multipliers

## Slide 3: Terminals on an Op Amp
Non-inverting
Input terminal
Inverting input
terminal
Output terminal
Positive power supply (Positive rail)
Negative power supply
(Negative rail)

## Slide 4: Op Amp Equivalent Circuit
vd = v2 – v1
A is the open-loop voltage gain
v2
v1
Voltage controlled voltage source

## Slide 5: Typical Op Amp Parameters
Parameter | Variable | Typical Ranges | Ideal Values
Open-Loop Voltage Gain | A | 105 to 108 | ∞
Input Resistance | Ri | 105 to 1013 W | ∞ W
Output Resistance | Ro | 10 to 100 W | 0 W
Supply Voltage | Vcc/V+ -Vcc/V- | 5 to 30 V -30V to 0V | N/A N/A

## Slide 6: How to Find These Values
Component Datasheets
  Many manufacturers have made these freely available on the internet
    Example: LM 324 Operational Amplifier

## Slide 8: dB
Decibels
Since P = V2/R
  10 log (P/Pref) or 20 log (V/Vref)
In this case:
20 log (Vo/Vin) = 20 log (A) = 100
A = 105 = 100,000

## Slide 10: Large Signal Voltage Gain = A
Typical
  A = 100 V/mV = 100V/0.001V = 100,000
Minimum
  A = 25 V/mV = 25 V/0.001V = 25,000

## Slide 11: Operational Amplifiers (Op Amps)
Ideal Op Amp
Non-inverting Amplifier
Unity-Gain Buffer
Inverting Amplifier
Differential Amplifier
Current-to-Voltage Converter
Non-ideal Op Amp

## Slide 12: Ideal Op Amp
1)
The open-loop gain, Av, is very large, approaching infinity.
2)
The current into the inputs are zero.

## Slide 13: Ideal Op Amp with Negative Feedback
Golden Rules of Op Amps:
The output attempts to do whatever is necessary to make the voltage difference between the inputs zero.
The inputs draw no current.

## Slide 14: Operational Amplifiers (Op Amps)
Ideal Op Amp
Non-inverting Amplifier
Unity-Gain Buffer
Inverting Amplifier
Differential Amplifier
Current-to-Voltage Converter
Non-ideal Op Amp

## Slide 15: Non-inverting Amplifier
Closed-loop voltage gain

## Slide 16: Operational Amplifiers (Op Amps)
Ideal Op Amp
Non-inverting Amplifier
Unity-Gain Buffer
Inverting Amplifier
Differential Amplifier
Current-to-Voltage Converter
Non-ideal Op Amp

## Slide 17: Unity-Gain Buffer
Closed-loop voltage gain
Used as a "line driver" that transforms a high input impedance (resistance) to a low output impedance. Can provide substantial current gain.

## Slide 18: Operational Amplifiers (Op Amps)
Ideal Op Amp
Non-inverting Amplifier
Unity-Gain Buffer
Inverting Amplifier
Differential Amplifier
Current-to-Voltage Converter
Non-ideal Op Amp

## Slide 19: Inverting Amplifier
Current into op amp is zero

## Slide 20: Operational Amplifiers (Op Amps)
Ideal Op Amp
Non-inverting Amplifier
Unity-Gain Buffer
Inverting Amplifier
Differential Amplifier
Current-to-Voltage Converter
Non-ideal Op Amp

## Slide 21: Differential Amplifier
Current into op amp is zero

## Slide 22: Differential Amplifier

## Slide 23: INVERTING SUMMING AMPLIFIER
R2
v3
v1
R1
v2
+
-
RF
vo
R3
0 V

## Slide 24: GAIN CALCULATIONS

## Slide 25: NON-INVERTING SUMMING AMPLIFIER
vO
v2
R3
RF
R2
v3
RA
R1
v1
+
-

## Slide 26
Integrating Op-Amp

## Slide 27: Differentiating Op-Amp
(where Vin and Vout are functions of time)

## Slide 28: Filters
Decouple the low-pass RC filter from the load. Uses: Simple audio. Remove frequencies over 20kHz (audible)

## Slide 29: Low-pass Filter (active)
Cutoff frequency
This works because the capacitor needs time to charge.