## Slide 1: University of Asia Pacific
Transducers
Md. Khairul Alam
Lecturer, EEE, UAP

## Slide 2: CONTENTS
WHAT IS TRANSDUCER
ELECTRICAL TRANSDUCER
CLASSIFICATION OF TRANSDUCERS
SELECTION CRITERIA OF THE TRANSDUCERS
BASIC CONSTRUCTION OF TRANSDUCERS
RESISTANCE TEMPERATURE DETECTOR
STRAIN GUAGE
APPLICATIONS,ADVATAGES AND DISADVANTAGES

## Slide 3: WHAT IS TRANSDUCER
A transducer is an electronic device that converts energy from one form to another (mechanical, visual, acoustic, electrical, thermal, chemical).
Example:
Microphones,
Loudspeakers,
Thermometers

## Slide 4
TRANSDUCER
Sensors (transducer which converts a measurable quantity (sound pressure level, optical intensity, magnetic field, etc) to an electrical voltage or an electrical current).
Actuators (transducer which converts an electrical signal into another form of energy, such as sound, pressure, light, mechanical movement).

## Slide 5: Transducers specifications
Range
Span
Error
Accuracy
Sensitivity
Nonlinearity
Resolution
Stability
Dead band/time
Response time

## Slide 6
Sensing Element: The physical quantity or its rate of change is sensed and responded to by this part of the transistor.
Transduction Element: The output of the sensing element is passed on to the transduction element. This element is responsible for converting the non-electrical signal into its proportional electrical signal.

## Slide 7: ELECTRICAL TRANSDUCERS
The electrical transducers is one which converts the non-electrical quantity into the equivalent electrical quantity.
Non-electrical quantity such as force, displacement, stress, temperature.
Electrical quantity such as current , voltage

## Slide 8: CLASSIFICATION OF TRANSDUCERS
On the basis of transduction form used.
As primary and secondary transducers.
As passive and active transducers.
As analog and digital transducers.
As transducers and inverse transducers

## Slide 9: ON THE BASIS OF TRANSDUCTION FORM USED
Resistive Transducers.
  Photoconductive Cell
  Thermistor
Capacitive Transducers.
  Capacitor microphone
  Dielectric gauge
Inductive Transducers.
  Magnetic circuit transducer
Voltage and current Generating Transducers.
  Hall effect pickup

## Slide 10: Passive and Active Transducers
If transducers derive the power require for transduction from an power source, then this kind of transducer are known as passive transducer
Example:
(1) LDR
(2) FSR
When there is no need for any source then these type of transducers are Active transducers
Example :
(1)Thermocouple
(2)Piezoelectric crystal

## Slide 11: Inverse Transducers
These type of transducers convert a electrical quantity into non-electrical quantity
Example
Piezoelectric crystal
Analog ammeter
Voltmeter

## Slide 12: Potentiometer
Angular and
Linear Position

## Slide 14: Strain Gauge
Convert physical deformation in the shape to resistance.

## Slide 15: Photoresistor

## Slide 16: Phototransistor

## Slide 17: Thermistors

## Slide 18: Thermoelectric sensors
Seebeck effect (When two dissimilar metal wires are connected at one end forming a junction, and that junction is heated, a voltage is generated across the junction (see the figure below).
Peltier effect (electrical current would produce heating or cooling at the junction of two dissimilar metals)

## Slide 19: Thermocouple

## Slide 20: Peltier plate

## Slide 21: SELECTION CRITERIA OF THE TRANSDUCERS
Operating principle
Sensitivity
Operating range
Accuracy
Errors
Environmental capability
Insensitive to unwanted Signal
Stability

## Slide 22: APPLICATION
Audio/video equipment
Pressure indication
Measurement of displacement
Alarms

## Slide 23: Thank You