## Slide 1: Microprocessor and Assembly Language Lecture Vol-4 Assembly Language Programming in 8086
CSE-311
Prof. A.H.M. Asadul Huq, Ph.D.

## Slide 2: Simple computer BLOCK DIAGRAM in terms of Assembly Language for 8086
System bus (shown in yellow) connects the various components of a computer.
CPU is the heart of the computer, most of computations occur inside the CPU.
RAM is a place to where the programs are loaded in order to be executed.
DEVICES: I/O devices like display, keyboard, et.

## Slide 3: INSIDE COMPONENTS OF CPU

## Slide 4: Review of 8086 Registers
8086 CPU has 8 general purpose registers
AX - the accumulator register (divided into AH / AL)
BX - the base address register (divided into BH / BL).
CX - the count register (divided into CH / CL):
DX - the data register (divided into DH / DL):
SI - source index register:
DI - destination index register:
BP - base pointer:
SP - stack pointer:

## Slide 5: Review of 8086 Registers, ... Cont.
SEGMENT REGISTERS
CS - points at the segment containing the current program.
DS - generally points at segment where variables are defined or data is stored.
ES - extra segment register, it's up to a coder to define its usage.
SS - points at the segment containing the stack.
Although it is possible to store any data in the segment registers, this is never a good idea. The segment registers have a very special purpose - pointing at accessible blocks of memory.

## Slide 6: How segment registers work?
Segment registers work together with general purpose register to access any memory value. For example if we would like to access memory at the physical address 12345h (hexadecimal), we should set the DS = 1230h and SI = 0045h. This is good, since this way we can access much more memory than with a single register that is limited to 16 bit values. CPU makes a calculation of physical address by multiplying the segment register by 10h and adding general purpose register to it (1230h * 10h + 45h = 12345h):
By default BX, SI and DI registers work with DS segment register; BP and SP work with SS segment register. other general purpose registers cannot form an effective address! also, although BX can form an effective address, BH and BL cannot.

## Slide 7: SPECIAL PURPOSE REGISTERS of 8086
IP - the instruction pointer:
Always points to next instruction to be executed
Offset address relative to CS
IP register always works together with CS segment register and it points to currently executing instruction.
FLAG
determines the current state of the processor.
They are modified automatically by CPU after mathematical operations, this allows to determine the type of the result, and to determine conditions to transfer control to other parts of the program.
Generally you cannot access these registers directly.

## Slide 8: Flags register of 8086
There are 9 active flag bits out of 16. The remaining 7 flags marked ‘U’ are undefined flags. These 9 flags are of two types: 6 Status flags and 3 Control flags

## Slide 9: Description of Flag bits
Status flags:
Carry flag (CF)- It is set whenever there is a carry or borrow out of the MSB (most significant bit) of a result. D7 bit for an 8 bit operation and D15 bit for a 16 bit operation.
Parity flag (PF)- It is set if the result has even parity. If parity is odd, PF is reset. This flag is normally used for data transmission errors.
Auxiliary carry flag (AC)-It is set if a carry is generated out of the lower nibble. It is used only in 8 bit operations like DAA and DAS.
Zero flag (ZF)- It is set if the result is zero.

## Slide 10: Description of Flag bits.. continued
Sign flag (SF)- It is set if the MSB of the result is 1. For signed operations such a number is treated as negative.
Overflow flag (OF)- It will be set if the result of a signed operation is too large to fit in the number of bits available to represent it. It can be checked using the instruction INTO (Interrupt on Overflow).
Control flags:
Trap flag (TF)- It is used to set the trace mode i.e. start single stepping mode. Here the microprocessor is interrupted after every instruction so that the program can be debugged.
Interrupt enable flag (IF)- It is used to mask (disable) or unmask (enable) the INTR interrupt. If user sets IF flag, the CPU will recognize external interrupt requests. Clearing IF disables these interrupts.
Direction flag (DF)- If this flag is set, SI and DI are in auto-decrementing mode in string operations.

## Slide 11: 8086 Instruction SET
The 8086 instruction set includes equivalents of the 8085 instructions plus many new ones.
The new instructions contain operations such as signed and unsigned multiplication and division, bit manipulation instructions, string instructions, and interrupt instructions.
The 8086 has approximately 117 different instructions with about 300 op-codes.
The 8086 instruction set contains: no operand, single operand, and two operand instructions. Except for string instructions which involve array operations, the 8086 instructions do not permit memory to memory operations.

## Slide 12
Functional groups of Instruction 8086 Instructions
The instructions of 8086 are classified into the following 6 functional groups:
Data transfer Instructions
Arithmetic and Logical Instructions
Branch Instructions
Processor Control Instructions
String Operation Instructions
Protection Control Instructions

## Slide 13
Register to a register
Immediate operand to a register
Immediate operand to the memory
Memory to a register
Register to a memory
Register to a segment register (excluding CS)
Memory to a segment register (excluding CS)
Register to an I/O port
I/O port to a register
Types of Data Transfer Instructions

## Slide 14: Data transfer Instruction MOV
Syntax: MOV dest, src
Function: Transfer data from register/memory/immediate to register/memory
dest  src
The instruction MOV transfers a byte or a word of data from the source to destination. The source can be a register or a memory location or an immediate number.
The destination can be a register or a memory location
Both the source and destination cannot refer to memory locations in the same instruction.
They must be of same data type, i.e., either of the type byte or type word.
Flags affected: None

## Slide 15
MOV
MOV CX, DX ; copies the 16-bit content of DX into CX.
MOV AH, AL ; copy 8-bit content of AL to AH
MOV AX, 0205H ; moves immediate data 0205H into 16-bit register AX.
MOV BX, [530BH] ; copy 16-bit data from the memory location 530BH to BX register
MOV DL, [BX]: moves the 8-bit content of memory location pointed to the address stored in BX to DL
Examples of Data Transfer Instructions

## Slide 16: Numerical Example OF MOV INSTRUCTIONS TO DISPLAY ASCII CHARACTER ‘A’ ON DOS WINDOW
here is a short program that demonstrates the use of MOV instruction:
ORG 100h ; this directive required for a simple 1 segment .com program.
MOV AX, 0B800h ; set AX to hexadecimal value of B800h.
MOV DS, AX ; copy value of AX to DS.
MOV CL, 'A' ; set CL to ASCII code of 'A', it is 41h.
MOV CH, 1101_1111b ; set CH to binary value.
MOV BX, 15Eh ; set BX to 15Eh.
MOV [BX], CX ; copy contents of CX to memory at B800:015E
RET ; returns to operating system.
RUN Result: ASCII character A is shown on DOS window

## Slide 17: Declaring Variables
Variable is a memory location whose content may be dynamically varied during run-time.
The assembler assigns a memory location to a variable (not visible to the user).
For a programmer it is much easier to have some value be kept in a variable named "var1" then at the address 5A73:235B, especially when you have 10 or more variables.
A classical compiler (eg. EMU 8086) supports two types of variables: BYTE and WORD (Assembler directives).
Syntax: <name DB value>; <name DW value>
name: can be any letter or digit combination, though it should start with a letter.
where, DB-Define Byte and DW-Define word.
value - can be any numeric value in any supported numbering system (hexadecimal, binary, or decimal).

## Slide 18: A MOV INSTRUCTION EXAMPLE USING VARIABLES
ORG 100h ; ORG is not an Instruction but just a directive to make a simple .com file (expands into no code).
MOV AL, Var1
MOV BX, Var2
RET ; stops the program.
Var1 DB 7 ; The assembler reserves one byte of memory for a variable named ;Var1 and initialize with value 7 during execution of the program
Var2 DW 1234h ; The assembler reserves two bytes of memory for a variable ; named Var2 and initialize with the value 1234h during execution of ;the program
-------------------------------------------
NOTE: Copy the above assembly code and try at home in EMU 8086

## Slide 19: Examples of Data Transfer Instructions ...Cont.
PUSH & POP
In 8086, the SP is decremented by 2 for PUSH and incremented by 2 for POP.
PUSH START [BX]: pushes the 16-bit contents of two memory locations starting at the 20-bit physical address computed from START, BX, and DS after decrementing SP by 2.
POP ES pops the top stack word into ES and then increments SP by 2.

## Slide 20: XCHG: Exchange Instruction
Syntax: XCHG dest, src
Function: Exchange the contents of the source and destination (dest <- -> src)
Description: XCHG swaps (exchanges) the contents of a source register or memory with the contents of a destination register or memory.
The source can be a register or a memory location. The destination can be a register or a memory location.
Both the source and destination cannot be memory locations in the same instruction.
They must be of the same data-type, i.e., either of the type byte or type word
Flags Affected: None

## Slide 21: Examples of XCHG Instructions
XCHG AX,CX; exchange the contents of registers AX and CX
XCHG AL, AMOUNT[BX]; exchange (8-bit) AL and memory AMOUNT[BX]
XCHG AX, AMOUNT[BX]; exchange (16-bit) AX and memory AMOUNT[BX]
XCHG BL, BH; exchange BL and AH
NOTE: The symbol AMOUNT used in the above examples is considered as an array of type word with size 100.

## Slide 22: IN: (Input from port) Instruction
Syntax: IN accumulator, port (or DX)
Function:
Input to AL (or AX) from I/O port
byte: AL <- [port];
word: AX <- [port], AH <- [Port+1]
Description: The instruction IN reads data from the port and copies into accumulator. AN 8-bit access to the port will place the data in AL register while a 16-bit access to port will place the data in AX register. The instruction IN has two formats: fixed port and variable port. Each of them can again be classified into an 8-bit or 16-bit access
Fixed port format: The address of a port is directly specified in the instruction
Variable Port Format: The address of a port is stored in the DX register before the instruction IN is executed. The advantage of the variable format IN instruction is that the port address can be loaded dynamically during the execution of a program
Flags Affected: None

## Slide 23: IN Instruction Examples
Fixed port format:
IN AL, 38H; input a byte (8-bit data) from the port address 38H to AL
IN AX, 38H; input a word (16-bit data) from the ports 38H and 39H to AX
Variable port Format (The port address is 16-bit and it is stored in the DX register):
MOV DX, 3124H; Initialize DX with the port address 3124H
IN AL,DX; reads 8-bit data from port pointed by DX (in this case 8-bit port 3124H) in AL
IN AX,DX; reads 16-bit data from the port whose address is already stored in DX (ports 3124H and 3125H) to AX

## Slide 24: OUT (Output to Port) Instruction
Syntax: OUT port (or DX), accumulator
Function:
Output from AL (or AX) to I/O port
byte: [port <- AL]
word: [port <- AL, [port+1] <- AH
Description: The instruction OUT writes the contents of the accumulator (AL for 8-bit and AX for 16-bit) to a specified port. The instruction OUT has 2 formats: fixed port format and variable port format. Each of them can again be classified into 8-bit or a 16-bit access.
Flags Affected: None

## Slide 25: Examples of OUT Instructions
Fixed Port Format (Direct Mode) (The address of a port is directly specified in the instruction)
OUT 38H, AL; copy 8-bit contents of AL register to port address 38H
OUT 38H, AX; copy 16-bit contents of AX register to port 38H and 39H.
Variable Format (Indirect Mode) (The port address is 16-bit and that is stored in the DX register before the instruction OUT is executed)
MOV DX, 3124H; Initialize DX with the port address 0F72H ([DX]=3124H)
OUT DX, AL; copy 8-bit contents of AL to the port pointed to by DX (in this case 3124H)
OUT DX, AX; outputs 16-bit data from AX (AL and AH) into ports 3124H and 3125H, respectively.

## Slide 26: XLAT (Translate a Byte) Instruction
Syntax: XLAT
Function: Translates a byte in AL using a table in the memory
AL <- DS:[BX+(AL)]
Description: This instruction replaces a byte in the AL register with a byte from the lookup table. Before execution of the XLAT instruction, BX should be loaded with the offset address of lookup table in the data segment (DS) and AL with the code to be converted. When, XLAT is executed, the byte pointed to by (BX-AL) is transferred to the AL register.
This instruction is used for translating characters from one code such as ASCII to another such as EBCDIC.
This instruction can be used to read the elements in a table.
In common applications you will hardly find any usage for XLAT
This is a no-operand instruction
Flags Affected: None

## Slide 27: LEA: LOAD EFFECTIVE ADDRESS
Syntax: LEA reg16, source
Function: Load effective address into a register.
reg16 <- (result of effective address or calculation of offset)
Description: The instruction LEA determines offset of a variable or a memory location indicated as a source (address) and places the offset in the specified 16-bit register.
Flags Affected: none

## Slide 28: Hexadecimal Number System Read <Assembly programming using EMU 8086.pdf>
Decimal (base 10) |  | Binary (base 2) |  | Hexadecimal (base 16)
0 |  | 0000 |  | 0
1 |  | 0001 |  | 1
2 |  | 0010 |  | 2
3 |  | 0011 |  | 3
4 |  | 0100 |  | 4
5 |  | 0101 |  | 5
6 |  | 0110 |  | 6
7 |  | 0111 |  | 7
8 |  | 1000 |  | 8
9 |  | 1001 |  | 9
10 |  | 1010 |  | A
11 |  | 1011 |  | B
12 |  | 1100 |  | C
13 |  | 1101 |  | D
14 |  | 1110 |  | E
15 1111 F |  |  |  | 
Hexadecimal System uses 16 digits:
0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F And thus the base is 16.
There is a convention to add "h" in the end of a hexadecimal number, this way we can determine that 5Fh is a hexadecimal number with decimal value of 95.
We also add "0" (zero) in the beginning of hexadecimal numbers that begin with a letter (A..F), for example 0E120h.
The hexadecimal number 1234h is equal to decimal value of 4660:

## Slide 29: Convert a Decimal Number into HEX
Steps:
Divide the decimal number by 16. Treat the division as an integer division.
Write down the remainder (in hexadecimal).
Divide the result again by 16. Treat the division as an integer division.
Repeat step 2 and 3 until result is 0.
The hex value is the digit sequence of the remainders from the last to first.
------------------- Example: Convert 195d into HEX -------
195/16=12(Res) + 3(Rem)
12(Res)/16=0(Res) +12(Rem)
So, HEX =>>12 3 =>> C3h Ans.

## Slide 30: NUMERICAL EXAMPLE OF LEA
If AX=1000, and BX=3; DI=AX=1000;
Then, LEA AX, [DI+BX] will produce AX=1000+3=1003=03EBh
--------------------------------------------------------------------------------------
The Assembly program:
org 100h ; defines where the machine code is to place in memory
MOV AX ,1000 ; AX=1000
MOV BX ,3 ; BX=3
MOV DI, AX ; DI=AX=1000
LEA AX, [DI+BX] ; Load effective address 100+3=1003 in AX
ret ; control is returned to the operating system
-------------------------------------------------------------------------------
ORG (abbr. for ORiGin) is an assembly directive (not an instruction). It defines where the machine code (translated assembly program) is to place in memory. As for ORG 100H this deals with 80x86 COM program format (COMMAND) which consist of only one segment of max. 64k bytes. 100H says that the machine code starts from address (offset) 100h in this segment

## Slide 31: Table of the list of data transfer instructions
OPCODE | OPERAND | EXPLANATION | EXAMPLE
MOV | D, S | D = S | MOV AX, [SI]
PUSH | D | pushes D to the stack | PUSH DX
POP | D | pops the stack to D | POP AX
PUSHA | none | put all the registers into the stack | PUSHA
POPA | none | gets words from the stack to all registers | POPA
XCHG | D, S | exchanges contents of D snd S | XCHG [2050], AX
IN | D, S | copies a byte or word from S to D | IN AX, DX
OUT | D, S | copies a byte or word from D to S | OUT 05, AL
XLAT | none | translates a byte in AL using a table in the memory | XLAT
LAHF | none | loads AH with the lower byte of the flag register | LAHF
SAHF | none | stores AH register to lower byte of the flag register | SAHF
PUSHF | none | copies the flag register at the top of the stack | PUSHF
POPF | none | copies a word at the top of the stack to the flag register | POPF
Here D stands for destination and S stands for source. D and S can either be register, data or memory address.

## Slide 32: Arithmetic and Logical Instructions
The 80X86 instruction set includes the instructions for performing arithmetic operations on numbers.
Arithmetic instructions generally involve 2 operands.
The source operand can be a register or memory location or an immediate number.
The destination can be a register or a memory location
Both the source and destination cannot refer to memory locations in the same instruction
They must be of the same data-type
Arithmetic instructions affect the CPU flags
Examples of arithmetic instructions are ADD, ADC, INC
Examples of logical instructions are NOT, OR, XOR, ETC.

## Slide 33: ADD: Addition
Syntax: ADD dest, src
Function: Add two operands and stores the result in dest
dest <- (src + dest)
Description: The instruction ADD adds the contents of the source to the destination and places the result in the destination
The source operand can be a register or memory location or an immediate number.
The destination can be a register or a memory location
Both the source and destination cannot refer to memory locations in the same instruction
Contents must be of the same data-type
Flags affected: AF, CF, OP, PF, SF, ZF

## Slide 34: Examples of ADD Instruction Statements
ADD AH, 09h ; AH  AH + 0 9h
ADD AX, 12h ; AX AX + 12h, (12h is converted to a word and added)
ADD BX, AX ; BX  BX + AX
ADD BX, [SI]; BX  BX + [SI], contents of memory location pointed to by SI in DS is added with BX and sum is placed in BX
ADD AL, BL

## Slide 35: Numerical Example of ADD Program
org 100h
MOV AL, 110d ; AL=110d
MOV BL, 85d ; BL=85d
ADD AL, BL ; AL <- 110+85=195d=C3h
ret
-------------------------------------
RUN RESULT:
AX=00C3 (195d)
--------------------------------------
Try this Add program in EMU 8086 and see the result in AX register !

## Slide 36: NUMERICAL Example of ADD instruction using Assembly Language
AL=01101110b=110d
BL=01010101b=85d
ADD AL, BL results in 195d (=C3h) and stored in AL replacing its old value (AL  AL + BL = 110 + 85 = 195d)
------------- The assembly program ------------
org 100h
MOV AL, 110 ; 110d = 6Eh
MOV BL, 85 ; 85d = 55h
ADD AL, BL ; Result: AL = 110d+85d=195d=C3h
ret
-----------------------
RESULT: Content of AL will be 195d = C3h

## Slide 37: ADC: Add with Carry
Syntax: ADC dest, src ;dest: memory or register src: memory, register, or immediate
Function in Brief: Add two operands with carry from previous add, and store the result in the dest
dest  (src + dest + CF)
Description: ADC is similar to ADD except, that the status of carry is added to the result.
Function: if (CF is 1), dest  (source + destination +1)
if (CF is 0), dest  (source + destination +0)
Flags Affected: AF, CF, OP, PF, SF, ZF

## Slide 38: Numerical ADC Example
org 100h
MOV AL,01
MOV BL,02
;Use instruction
;CLC to clear carry flag, that is set CF=0 or
;STC to set carry flag, that is set CF=1
STC ;
ADC AL,BL
ret
----------------------
Result: AL=3 (if CLC is used)
AL=4 (if STC is used)

## Slide 39
Arithmetic and Logical Instructions
ADC Examples
ADC dest, src
ADC AH, 09H
ADC AX, 12H
ADC BX, AX
ADC BX, [SI]
ADC AX, AMOUNT[BX]
ADC [BX], DX

## Slide 40
Arithmetic Instructions (Cont..)
SUB dest, src
SUB AH, 09H
SUB AX, 12H
SUB BX, AX
SUB BX, [SI]
SUB AX, AMOUNT[BX]
SUB [BX], DX
SUB: Subtraction

## Slide 41
Arithmetic and Logical Instructions (Cont..)
SBB dest, src
SBB AH, 09H
SBB AX, 12H
SBB BX, AX
SBB BX, [SI]
SBB AX, AMOUNT[BX]
SBB AMOUNT[BX], DX
SBB: Subtraction with Borrow

## Slide 42: INC : INCREMENT
Examples | 
INC AL | AL AL+1
INC AX | AX  AX+1
INC BYTE PTR [BX] | The byte pointed to by the register BX is incremented by 1
INC WORD PTR [BX] | The word pointed to by the register BX is incremented by 1
INC AMOUNT[BX] | BX is an array index, word increment is performed
Syntax: INC dest, add one to dest (reg or r/m), dest  (dest + 1)
Description:
The INC instruction one to the specified register or memory location and stores the result in the destination.
Flags Affected: AF, OF, PF, SF, ZF
Carry Flag: Not affected
Also, DEC (Decrement) is similar to INC (dest  dest - 1)

## Slide 43: MUL : MULTIPLICATION
When two single bytes are multiplied −
The multiplicand is in the AL register, and the multiplier is a byte in the memory or in another register. The resultant product is saved in AX. High-order 8 bits of the product is stored in AH and the low-order 8 bits are stored in AL. (Result is 16 bit)
When two one-word values are multiplied −
The multiplicand should be in the AX register, and the multiplier is a word in memory or another register. For example, for an instruction like MUL DX, you must store the multiplier in DX and the multiplicand in AX.
The resultant product is a doubleword, which will need two registers. The high-order (leftmost) portion gets stored in DX and the lower-order (rightmost) portion gets stored in AX. (Result is 32 bit)
Syntax: MUL src; Multiply Accumulator value (AL/AX) by unsigned value in reg/mem.
byte: AX (AL * src8), word: DX:AX (AX * src16)
The instruction affect the Carry and Overflow flag

## Slide 44: MUL Examples
MUL BH | ; AX  AL * BH (8-bit multiplication and high byte in AH)
MUL BX | ; DX:AX  AX * BX (16-bit multiplication and high word in DX)
MOV AX, MULTIPLICAND_16 MOV CL, MULTIPLIER_8 MOV CH, 00H MUL CX | AX  16 bit multiplicand CL  8 bit multiplier CH  0, upper byte of CX is set to zero DX:AX  AX * CX (32 bit result in DX and AX
Numerical example of MUL code for EMU8086
---------------------------------------------------------------------
org 100h
MOV AX,3039h ; 3039h = 12345d, 16-bit(binary) multiplicand
MOV CL,78h ; 78h = 120d, 8-bit (binary) multiplier
MOV CH,00h ; CH is set to 0
MUL CX ; DX:AX <- AX * CX (32-bit result is stored in DX and AX)
; The answer is DX:AX=0016-9AB8h
ret
Output:
3039h*0078h=DX:AX=0016:9AB8h=1481400d. (12345d * 120d=1481400d)

## Slide 45: DIV: Division Instruction
Syntax: DIV src ; (src can be a register or a memory location)
byte: AL  (AX/src8); AH  AX MOD src8 (reminder)
word: AX  (DX:AX/src16); DX  DX:AX MOD src16 (reminder)
The division operation generates two elements - a quotient and a remainder. In case of multiplication, overflow does not occur because double-length registers are used to keep the product. However, in case of division, overflow may occur. The processor generates an interrupt if overflow occurs.
The dividend is in an accumulator. DIV instruction can work with 8-bit, 16-bit (or 32-bit) operands. The operation affects all six status flags. Following section explains two cases of division with different operand size −

## Slide 46: 16-bit dividend (ভাজ্য)
When the divisor is 1 byte (8-bit) −
The dividend is assumed to be in the AX register (16 bits). After division, the quotient goes to the AL register and the remainder goes to the AH register.

## Slide 47: 32-bit dividend (ভাজ্য)
When the divisor is 1 word (16-bit)
The dividend is assumed to be 32 bits long and in the DX:AX registers. The high-order 16 bits are in DX and the low-order 16 bits are in AX. After division, the 16-bit quotient goes to the AX register and the 16-bit remainder goes to the DX register.

## Slide 48
Logical Instructions
AND dest, src
AND AH, CH
AND BX, 00FFH
AND CX, [SI]
OR AH, CH
OR BX, 00FFH
OR CX, [SI]
AND: Logical AND, OR: Logical OR, XOR: Logical Ex-OR
XOR AH, CH
XOR BX, 00FFH
XOR CX, [SI]
NOT: Logical NOT
NOT dest
NOT AL
NOT BX
NOT [BX]

## Slide 49: Assembly code for HELLO WORLD !!
DATA SEGMENT
MESSAGE DB "HELLO WORLD!!!$"
ENDS
CODE SEGMENT
ASSUME DS:DATA CS:CODE
START:
MOV AX,DATA
MOV DS,AX
LEA DX,MESSAGE
MOV AH,9
INT 21H
MOV AH,4CH
INT 21H
ENDS
END START

## Slide 50: Assembly code for HELLO WORLD with explanation of statements
DATA SEGMENT ; DATA – name of user defined segment
MESSAGE DB "HELLO WORLD!!!$” ; MESSAGE – Pointer to the string
ENDS ; End of DATA Segment
CODE SEGMENT ; CODE – Name of the user defined segment
ASSUME DS:DATA CS:CODE ; Initialize CS and DS to the code segment
START:
MOV AX, DATA ; Initialize DS to the code segment
MOV DS, AX
NOTE: Read the document ”Explanation of Assembly Code for Hello World.doc” on my website.

## Slide 51: Assembly code for HELLO WORLD
LEA DX, MESSAGE ; Load effective address of MESSAGE into DX
MOV AH, 9 ; display string function
INT 21H ; Call DOS service
MOV AH, 4CH ;
INT 21H ; In MS-DOS, interrupt 21h and function 4ch causes the ; current process to terminate.
ENDS ; End of segment
END START ; End of program

## Slide 52: Microprocessors and Assembly Language
THE END
THANK YOU AND GOOD LUCK

## Slide 53: CT-4
Date: 30-01-2019
Syllabus: Vol-4
Question type: Short questions
Total Marks: 20
Note: Participation is not mandatory
Roll call: Yes