## Slide 1
Computer Graphics
Hidden Surface Removal

## Slide 2: Rendering Pipeline
modelling of geometry
transformation into world coordinates
placement of cameras and light sources
backface culling
projection
clipping w.r.t. view volume
hidden surface removale (hsr)
rasterization
illumination and shading
transformation into camera coordinates

## Slide 3: Hidden Surface Removal

## Slide 4: Hidden Surface Removal: Motivation
goals:
  model parts independently processed
  show visible parts only
    parts facing the camera
    parts not obscured by other objects

## Slide 5: Back Face Culling
In a solid object, there are surfaces which are facing the viewer (front faces) and there are surfaces which are opposite to the viewer (back faces).
back faces:
  polygons that do not ‘face’ the camera
  (usually) not visible
remove (‘cull’) these
  reduce polygon count by ~ ½ of the total polygon number (on average)

## Slide 6: Back Face Culling
zv
xv
yv
Vview
N=(A,B,C)
A polygon is a backface if
Vview . N >0

## Slide 7: Back Face Culling
v = (-1, 0, -1)
n2 = (-3, 1, -2)
n1·v = (2, 1, 2) · (-1, 0, -1)
= -2 – 2 = -4,
so n1·v < 0
so n1 front facing polygon
n1 = (2, 1, 2)
n2 ·v = (-3, 1, -2) · (-1, 0, -1)
= 3 + 2 = 5
so n2 · v > 0
so n2 back facing polygon

## Slide 8: Back Face Culling
Each surface has a normal vector. If this vector is pointing in the direction of the center of projection, it is a front face and can be seen by the viewer. If it is pointing away from the center of projection, it is a back face and cannot be seen by the viewer.
If the viewpoint is on the +z axis looking at the origin, we only need check the sign of the z component of the object’s normal vector
  if nz < 0, it is back facing
  if nz > 0 it is front facing
  What if nz = 0?
    the polygon is parallel to the view direction, so we don’t see it

## Slide 9: Back Face Culling
is back face culling enough?
  no, when objects in the scene overlap partially
remaining front-facing polygons must be rendered in the ‘right’ order  need an extra HSR technique (see next)

## Slide 10: HSR: Painter’s Algorithm
simulate the way actual painters work
  draw scene from back to front
sort scenes polygons from back to front
start rendering polygons from the back
problems:
  cyclic overlaps
  sorting is O(n log n)
  works only for polygons

## Slide 11: z-Buffering
idea:
  use advantages of painter’s algorithm (back to front rendering)
  avoid its disadvantages (sorting polygons)
implementation:
  trade memory (cheap) for speed (critical)
  trade accuracy for speed (fast rendering, imperfect Z (depth) estimation)

## Slide 12: z-Buffering
introduce new per-pixel buffer: z-buffer (in addition to the image frame buffer)
z-buffer: stores z-values of pixels

## Slide 13: z-Buffering
treat each primitive (triangle) individually: scene  objects  triangles  pixels
use z-buffer to check whether each pixel of each triangle is hidden or not
at any time, the polygons rendered so far are correctly ‘hidden’

## Slide 14: z-Buffering: Algorithm
z-buffer = very small negative number //clear z-buffer
for each triangle T
  project all vertices of T on camera plane
  interpolate z-values at each pixel p (scan line)
  if (z-buffer[p] < z(p)) //p not hidden
    z-buffer[p] = z(p)
    framebuffer[p] = desired color for p
The z-coordinates (depth values) are usually normalized to the range [0,1]
after scene processing z-buffer contains depth map of scene

## Slide 15: z-Buffering: Example
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-1
-3
-2
-5
-4
-3
-7
-6
-5
-4
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
=
+
-1
-2
-3
-3
-4
-4
-5
-1
-2
-3
-3
-4
-5
-4
-5
-6
-7
-1
-3
-2
-5
-4
-3
-7
-6
-5
-4
-1
-2
-3
-3
-4
-5
-4
-5
-6
-7
-1
-3
-2
-5
-4
-3
-7
-6
-5
-4
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
=
=
=
+
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-1
-3
-2
-5
-4
-3
-7
-6
-5
-4
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-1
-3
-2
-5
-4
-3
-7
-6
-5
-4
-1
-2
-3
-3
-4
-4
-5
-1
-2
-3
-3
-4
-5
-4
-5
-6
-7

## Slide 16: z-Buffering
advantages
  speed: direct hardware implementation
  speed: no primitive sorting needed (only need to know distance to camera)
  generality: can handle any primitive (works per-pixel, not per-primitive!)
disadvantages
  needs memory to keep the z-values (e.g. 1024x1024x32 bit = 4MB)
  cannot handle transparency properly

## Slide 17: Other HSR Algorithms
hierarchical z-buffer
Appel’s algorithm (for lines)
Warnock's algorithm
Octrees
Binary Space Partitioning (BSP-trees)
A-buffer (with anti-alising)