## Slide 2
Electric Motors
Introduction
DC Motors
AC Motors
Synchronous Motors
Induction Motors
Conclusion

## Slide 3
Introduction
In this lecture we consider various forms of rotating electrical machines
These can be divided into:
  generators – which convert mechanical energy into electrical energy
  motors – which convert electrical energy into mechanical energy
Both types operate through the interaction between a magnetic field and a set of windings

## Slide 4
DC Motors
A DC Motor is a very simple electric motor which is operated on direct current (DC). The DC Motor moves due to the torque generated by the electro-magnetic field. A simple DC Motor uses electric coil and magnets of opposite polarity. As the magnets with opposite poles attracts and repels one another, a DC Motor turns. The electric coil used in a DC Motor acts as an electromagnet

## Slide 5
DC motor characteristics
  many forms – each with slightly different characteristics
  again can be permanent magnet, or series-wound, shunt-wound or compound wound
  figure below shows a shunt-wound DC motor

## Slide 6
AC Motors
An AC motor is an electric motor driven by an alternating current (AC). The AC motor commonly consists of two basic parts, an outside stationary stator having coils supplied with alternating current to produce a rotating magnetic field, and an inside rotor attached to the output shaft producing a second rotating magnetic field.
AC motors can be divided into two main forms:
  synchronous motors
  induction motors

## Slide 7
Synchronous motors
  just as a DC generator can be used as a DC motor, so AC generators (or alternators) can be used as synchronous AC motors
  three phase motors use three sets of stator coils
    the rotating magnetic field drags the rotor around with it
  single phase motors require some starting mechanism
  torque is only produced when the rotor is in sync with the rotating magnetic field

## Slide 8
Induction motors
  these are perhaps the most important form of AC motor
  rather than use slip rings to pass current to the field coils in the rotor, current is induced in the rotor by transformer action
  the stator is similar to that in a synchronous motor
  the rotor is simply a set of parallel conductors shorted together at either end by two conducting rings

## Slide 9
Both DC and AC motors are used
  high-power motors are usually AC, three-phase
  domestic applications often use single-phase induction motors
  DC motors are useful in control applications

## Slide 10
Conclusion

## Slide 11
THANK YOU